Electronic and Magnetic Structures of the Post-perovskite-type Fe2O3 and Implications for Planetary Magnetic Records and Deep Interiors

Sang-Heon Dan Shima, Amelia Bengtsonb, Dane Morganb, Wolfgang Sturhahnc, Krystle Catallia, Jiyong Zhaoc, Michael Lerchec,d, and Vitali Prakapenkae

a Massachusetts Institute of Technology; b University of Wisconsin; c Argonne National Laboratory; d Carnegie Institution of Washington; and e University of Chicago

This figure shows changes in magnetic and crystal structures of hematite with pressure. (Left) corundum-type structure at low pressure, (Middle) Rh2O3-II-type structure at intermediate pressure, and (right) post-perovskite-type structure at high pressure.

Hematite (Fe2O3) is used for deciphering paleomagnetism and is an important proxy for the phases in Earth’s mantle and core.  It has been proposed that impact would demagnetize the record carrier minerals and pressure is believed to change the spin state of iron from high spin to low spin in the mantle.  Combining high-pressure synchrotron experiments (Shim) and ab initio calculations (Morgan), we showed that hematite undergoes a phase transition to the post-perovskite phase at high pressure, similar to the dominant mantle phase MgSiO3.  More importantly, we found that the spin state changes in a complex manner: high spin → low spin → mixed spin (both high and low spins) with pressure, suggesting that Fe concentration and spin may be an important factor in the transitions.  In addition, hematite undergoes complex magnetic transitions with pressure: magnetic → non-magnetic → magnetic, which would influence the magnetic records during shock events.

The result is published in “Shim et al. (2009) Proceedings of the National Academy of Sciences 106, 5508-5512” and featured in “In This Issue, Proceedings of the National Academy of Sciences 106, 5451-5452”.

This work was supported by the National Science Foundation (NSF) Grants EAR0738655 to Dan Shim and EAR0738886 to Dane Morgan. Measurements were performed at Sectors 3 and GeoSoilEnviro-Cars (GSECARS) at Advanced Photon Source. GSECARS is supported by the NSF and DOE. Use of Sector 3 was also supported by the Consortium for Materials Properties Research in Earth Sciences (COMPRES) under NSF Cooperative Agreement EAR 06-49658. Use of the APS was supported by the DOE.